## Slide 1: L&L: PE TCL Characterization scripts
Daniel Bertrand
June 5, 2015

## Slide 2: Outline
PE_COMMON Vault TCL scripts
    Register namespace
    Equipment Namespace
    Visa
    Bit manipulation
  Other TCL Scripts
    Teacup command
    Controlling Windows apps (COM)
    Controlling other TCL instances.

## Slide 3: TCL at PMC
TCL used +10 years in PE, adopted from PV groups
Also used in by PD for controlling simulators
BWD is moving to python (but still need TCL for ATP cmd file generation)
Pros:
Interactive, the “cmd args..” prefix style is similar to a unix shell
Very dynamic (ex: functions can be redefined, deleted, renamed)
Very permissive BSD style license.
Cons:
Has been falling out of popularity for many years.
the “cmd args..” prefix style is unlike other programming languages

## Slide 4: PE_COMMON Vault
PE “Common” SVN vault is located here:
http://bby-pv-svn04:24002/svn/PM26_98_11_A/trunk
It contains a master copy of generic TCL that’s needed for most projects:
USB dongle drivers (jtag, SPI, I2C/TWI)
Equipment control library
Standard register namespace lookup code
Libraries for bit manipulation, puts_colour, etc.

## Slide 5: PE_COMMON Vault
Populating a new project vault with these scripts?
Keep it simple: copy a snapshot into your project vault
If you have improvements, commit it back up stream to the common vault

## Slide 6: Register namespace
The PE register namespace code has a few important features for us:
export to tester command files
“Offline” mode (for resim testbench before silicon)
wrRd BLOCK::SUBBLOCK::REG::BIT
wrRd BLOCK::SUBBLOCK::REG::BIT 0x1234

## Slide 7: Register namespace
Instance fan-out rules are not currently well documented:
Read/write to range of instances:
::DEV_TOP::C8_SERDES(0:7)::CNI_UNI_TXRX_MTSB
Read/write to several instances:
::DEV_TOP::C8_SERDES(2,6,1)::CNI_UNI_TXRX_MTSB

## Slide 8: Register namespace
Nested instances are more complicated:
BLOCK(0/19)::SUBBLOCK(0/1)::REG::BIT -> expands to all nested permutations:
BLOCK(0)::SUBBLOCK(0)::REG::BIT
BLOCK(0)::SUBBLOCK(1)::REG::BIT
BLOCK(19)::SUBBLOCK(0)::REG::BIT
BLOCK(19)::SUBBLOCK(1)::REG::BIT
BLOCK(0,19)::SUBBLOCK(0,1)::REG::BIT -> expands to all parallel combinations:
BLOCK(0)::SUBBLOCK(0)::REG::BIT
BLOCK(19)::SUBBLOCK(1)::REG::BIT

## Slide 9: Register namespace
Sub-bitfield ranges are accessible:
BLOCK::SUBBLOCK::REG::BITFIELD(7:4)
BLOCK::SUBBLOCK::REG::BITFIELD(5)
Whole register are also accessible:
BLOCK::SUBBLOCK::REG:: (Omit the bitfield name)

## Slide 10: Register Namespace
Locate bits using “f” or “nameSearch” commands

## Slide 11: Equipment Namespace
Most of the equipment code is encapsulated into TCL namespaces, the advantage is:
Makes it easy to locate procs
Multiple copies can be instantiated (control of multiple of the same type of equipment )
For the power supplies, a consistent API is provided - allows power supplies to be substituted easily.

## Slide 12: Equipment Namespace
E3631
E3633
"apply P6V,1.0,0.3"
"apply 1.0,0.3"
Incompatible SCPI commands
E3631 is triple output
Compatible tcl API
::AVD::setVoltCurr 1.0,0.3
::AVD::setVoltCurr 1.0,0.3
Bench #1
Bench #2

## Slide 13: Equipment Namespace(2)
To instantiate an equipment, a “new” procedure is used, e.g
newE3633A ::AVD:: 5
newE3633A ::VDD:: 4
Some power supplies have multiple outputs, this is specified by an additional argument:
newE3631A ::AVD:: 5 P6V
newE3631A ::VDDO:: 5 P25V

## Slide 14: Equipment Namespace(3)
Inside the namespace a consistent set of procedures are provided:
setVolt (output voltage)
setCurrent (current limit)
outputOn/outputOff
setCurrentProtection (if hardware is not available this is an empty proc)
Etc..

## Slide 15: What is VISA?
Virtual Instrument Software Architecture
VISA is an instrument control library that supports multiple I/O interfaces
Uses the familiar SCPI
VISA
C-API
GPIB
USB
Ethernet
PXI
serial
TCL VISA wrapper
User script

## Slide 16: TCL Visa Library
The TCL-VISA library is an open source library:
http://tclvisa.sourceforge.net/
Some in-house tcl wrapper code is provided to create backwards compatible ::gpib::* commands.
Prerequisites:
The visa32.dll needs to be installed on the lab PC. (Is installed by Agilent Connection Expert, or National Instrument’s software).

## Slide 17: TCLVISA example
TCLVISA uses tcl’s channel I/O api
It has an open command which returns a file handle
You then use the familiar puts, gets, read & close commands
Example visa transaction:
set vi [::visa::open $::visa::rm $VisaAddress]
puts $vi "*IDN?"
set ret [gets $vi]
puts "Instrument IDN is: $ret"
close $vi

## Slide 18: TCL Visa Library (PE enhancements)
The legacy IBWrite/IBQuery/IBRead command updates:
Now accepts visa addresses in addition to the raw GPIB address.
Variable ::gpib::disable_remote_mode, controls whether access to the GPIB equipment is done in remote mode (= 0, default) or local mode (=1)
Variable ::gpib::timeout_ms controls the timeout period (default is 5000ms).
New command ::gpib::send_all_to_local puts GPIB connected equipment into local mode.

## Slide 19: TCL Visa Library(Visa addresses)
Example USB Visa address:
USB0::0x0957::0x5010::MY49101016::INSTR
USB0 == USB connected (other possibilities are GPIB, TCPIP, ASRL)
0x0957 == Agilent Mfg ID
0x5010 == J-BERT N4903B Model ID
MY49101016 == Serial number
INSTR == this is an instrument (other possibility is INTFC, for e.g. the gpib interface controller)

## Slide 20: TCL Visa Library(Visa addresses)
Find Visa Address
This will return a list of all connected equipment:
::visa::find $::visa::rm "?*"
Or a convenient alternative:
::gpib::find_all
To match a specific instrument:
::visa::find $::visa::rm "USB?*::0x0957::0x5010?*" -> this finds all USB connected J-BERTS
(?* is VISA regexp syntax meaning match one or more chars)

## Slide 21: Bit manipulation
TCL internally represents integers using signed 32bit ints (2’s compliment)
For values too large for 32bits it uses a “bignum” format.
Values are converted between Bignum/int32 automatically as-need

## Slide 22: Bit manipulation
How to convert to “hex” or “binary”?
Hex and binary are ascii string representation
You need the tcl equivalent of sprintf: “format”
Format specified is almost identical to C’s
Tcl8.6.x adds %b for binary

## Slide 23: Bit manipulation
How to convert back from these string representation?
TCL accepts inputs like “0b0101” “0x1A32” almost everywhere a number is expected

## Slide 24: Bit manipulation
Many legacy PMC integer formatting scripts are not needed
They are also buggy, slow, and don’t support Bignum
Some example names of these scripts that occasionally remake a reappearance:
dec2bin, bin2dec, dec2hex, hex2dec, hexNibble2binNibble, binNibble2hexNibble, hexReg2binReg, binReg2hexReg
For tcl 8.5.x, dec2bin is required as format did not have “%b”

## Slide 25: 2’s compliment
Functions are provided for 2’s compliment sign extension and contraction (“extend2scomp” and “contract2scomp”)
Contraction is straight forward (drop MSBs - AND with a mask).
Extension requires replication of the sign bit into the MSBs
Example sign extension:

## Slide 26: 2’s compliment
Example usage:
Similar functions are provided for sign-magnitude formats

## Slide 27: Other scripts in PE Vault
puts_colour.tcl -> colour printing to the console (you can also change font)
try.tcl -> a backport for tcl8.5.x of the “try” command (8.6.x)
simpleplot.tcl -> for making quick & dirty XY-plots, etc.
svn.tcl -> check and warn users if their local svn copy is outdated.
pe_tkcon.tcl -> adds improved tab-autocompletion, other tkcon improvements
Parse_args.tcl -> A copy of CBU PV’s command argument parser

## Slide 28: Some additional TCL packages

## Slide 29: Installing additional TCL Packages
ActiveState TCL has a large collection of optional packages
Manage these with windows “teacup.exe” command
It has subcommands for search, install, remove, update.
Example:
teacup search <search string>
teacup install <packagename>

## Slide 30: Control Windows Applications
TCOM - TCL interface to window’s COM interface
You can control windows apps (excel, word, etc) from tcl

## Slide 31: Controlling another TCL instance
Example use case:
Digi120G char required automation of PV’s setup (for datapath timing screens)
PE Char board
PV comExpress
(Linux)
PCIe
PE Lab PC
JTAG/I2C
TCL On Lab PC controlled 2nd TCL instance running on ComExpress
(Lab network)

## Slide 32: Controlling another TCL instance
“comm” package: commands from the top console are executed in the second console.
Note: May need to brace with { } to avoid substitution before sending

## Slide 33: Closing opened Files
Common lab user frustration:
Script crashes before closing a file handle.
File is locked, unable to delete or move file without killing tcl
Solution: chan names

## Slide 34: Questions?